## Slide 1
Ultrasound Image Enhancement Pipeline
Speckle Despeckling and CLAHE Feature Enhancement
for Breast Ultrasound Segmentation Preprocessing
Eastwood Tweneboah Osei | University of Ghana — Final Year Project | BUSI Preprocessing for AMFU-Net Adaptation

## Slide 2
Why Ultrasound Images Need Enhancement
Ultrasound is the most widely used non-invasive diagnostic imaging modality
But raw B-mode frames have two persistent problems:
  Low contrast — histograms are skewed toward low intensities
  Multiplicative speckle noise — degrades fine detail, edges, and lesion boundaries
Filtering out speckle on its own induces blurring and destroys structure that matters for diagnosis
Goal: suppress speckle, then enhance features — in that order
I(x,y) = J(x,y) × N(x,y)
Observed image = clean tissue signal × multiplicative speckle field
Speckle is not additive Gaussian noise — it multiplies the underlying signal, so simple subtraction-based filters do not remove it cleanly.
2

## Slide 3
Two-Stage Processing Pipeline
Raw
Ultrasound
Frame
Stage 1
Despeckling
Stage 2
CLAHE
Enhancement
Enhanced
Frame
Segmentation
Network
(MFEF + DAG)
Stage 1 removes multiplicative speckle noise; Stage 2 recovers and enhances local contrast and edges that speckle filtering tends to blur.
This notebook pipeline outputs an enhanced single-modality image feeding directly into a segmentation backbone (see slide 12).
3

## Slide 4
Stage 1 — Speckle Despeckling
Speckle model: I = J × N (N = multiplicative speckle field to be estimated / removed)
Classical — Lee Filter (default)
Adaptive local-statistics filter
Local coefficient of variation: Ci = σ / μ, within a sliding window
Homogeneous regions (low Ci) → smoothed toward the local mean
Feature / edge regions (high Ci) → left mostly unchanged
No training data required — usable immediately
CNN-Based (paper's method, optional)
3-layer network: Conv+ReLU → Conv+ReLU → Conv+BN+Tanh
Learns to estimate the multiplicative speckle field N̂
Despeckled image = I / N̂
Trained on synthetically generated speckle pairs (no real paired data needed)
Available as an alternative once trained
4

## Slide 5
Stage 2 — Why CLAHE, Not Plain Equalization
Global histogram equalization stretches contrast using the whole image — fails when the histogram is skewed, as ultrasound typically is
Adaptive Histogram Equalization (AHE) equalizes small tiles independently — but over-amplifies speckle noise in flat regions
CLAHE clips each tile's histogram at a limit before equalizing — local contrast is enhanced without letting noise explode
clip limit
Excess above the clip limit is redistributed across the tile's histogram bins before the transform is computed.
Tile histogram (schematic)
5

## Slide 6
Automatic Tile Sizing via Image Entropy
E = − Σ pk log2(pk), k = 0..255
s = (M − Emax) e^(−λE) + Emax
High entropy (detailed, textured frame) → small tiles (~8×8 px) for fine local adaptation
Low entropy (near-uniform frame) → tiles up to M/2, avoiding unnecessary local processing
λ = 0.7, Emax = 8 bits — pipeline defaults
High entropy →
fine tile grid
Low entropy →
coarse tile grid
6

## Slide 7
Target Distributions and Interpolation Kernels
3 Target Histogram Shapes (per tile)
Uniform — classic histogram equalization
Rayleigh — out = α√(2 ln(1/(1−cdf)))
Exponential — out = −α ln(1−cdf)
Clip limit controls aggressiveness: too high → oversaturated; too low → flat
3 Interpolation Kernels (blend tiles)
Bilinear — nearest 2×2 tiles, linear weights
Cubic — 4×4 tile neighborhood, smoother transitions
Lanczos-3 — 6×6 tile neighborhood, sharper detail preservation
3 distributions × 3 kernels = 9 combinations evaluated
Pipeline default — Rayleigh distribution + Lanczos-3 interpolation, clip limit ≈ 0.01 (see next slide for why)
7

## Slide 8
Why Rayleigh + Lanczos-3 Performs Best
Rayleigh statistics naturally model the amplitude distribution of fully-developed ultrasound speckle — matching the target shape to the tissue's underlying physics avoids an artificial-looking contrast stretch
A low clip limit (≈ 0.01) keeps the transform close to identity in flat regions, enhancing contrast mainly where local structure already exists
Lanczos-3's wider support and sharper roll-off blends neighboring tile transforms with less block artifact than bilinear or cubic interpolation
Confirmed by both radiologist subjective scoring (highest among 9 combinations) and objective SSIM / EPI / UQI metrics
8

## Slide 9
Measuring Enhancement Quality
Metric | What It Measures | Good Value
PSNR | Pixel-level fidelity vs. a reference frame (decibels) | Higher is better
SSIM | Structural similarity — luminance, contrast, structure | Close to 1
EPI | Edge preservation index — how well edges survive processing | Close to 1
UQI | Combined contrast, luminance, and correlation distortion | Close to 1
All four metrics are used in the comparative analysis (Section 7 of the accompanying notebook) to score the 9 CLAHE distribution × interpolation combinations.
9

## Slide 10
Dataset — BUSI (Breast Ultrasound Images)
~780 breast ultrasound images from 600 female patients, collected in 2018 at Baheya Hospital, Cairo, Egypt
3 classes: normal, benign, malignant — each image paired with an expert-annotated ground-truth segmentation mask
A widely used public benchmark for breast ultrasound segmentation research
Why used here:
  Ground-truth masks are needed to train and evaluate the downstream segmentation network
  Realistic clinical speckle and contrast characteristics — a genuine testbed for this preprocessing pipeline
  Known limitation: prior audits report image/annotation quality issues in a meaningful share of the set (roughly 40%), so a cleaning pass precedes use
10

## Slide 11
Where This Fits — Preprocessing for AMFU-Net
BUSI
Frame
Despeckle +
CLAHE
(this pipeline)
Enhanced
Single-Channel
Input
MFEF + DAG
Segmentation
Network
Predicted
Mask
Replaces the original dual-modality fusion stage of AMFU-Net with single-modality despeckling + CLAHE preprocessing
Feeds directly into the unchanged MFEF (multi-scale feature extraction and fusion) + DAG segmentation backbone
12

## Slide 12
Summary
Two-stage pipeline: despeckle (Lee filter / CNN) → CLAHE (entropy tile sizing + Rayleigh distribution + Lanczos-3 interpolation)
Reduces speckle noise while enhancing diagnostically relevant contrast and edges
Validated end-to-end on synthetic data; BUSI selected for real-data evaluation and downstream segmentation
Feeds directly into the AMFU-Net-based segmentation pipeline as the single-modality preprocessing stage
Next steps: clean the BUSI subset, run the 9-combination comparative analysis on real frames, and integration-test with the MFEF + DAG backbone
13